## Slide 1: The da Vinci Research Kit (dVRK): System Description: Mechatronics
Peter Kazanzides
Research Professor
July 15, 2024

## Slide 2: Outline
da Vinci Research Kit (dVRK)
Next generation dVRK-Si and controller

## Slide 3: Medical Robotics Research
The da Vinci Surgical System is available to surgeons, but what is available to researchers?
Raven II robot (Applied Dexterity)
da Vinci Surgical System, © 2022 Intuitive Surgical, Inc.
da Vinci “Read only” Research API

## Slide 4: da Vinci Research Kit
Mechanical components from decommissioned da Vinci surgical robots
Consortium for “open source” controllers
  JHU: software, controller electronics
  WPI: controller power, packaging, assembly
  ISI: Interface electronics
P. Kazanzides, Z. Chen, A. Deguet, G. Fischer, R. Taylor, S. DiMaio, “An open-source research kit for the da Vinci® surgical system”, ICRA 2014.

## Slide 5: Historical Origin, 2003-2004
Low Power Motor Controller (LoPoMoCo)
Snake Robot, Nabil Simaan (JHU)
Kapoor, Simaan, Kazanzides, “A system for speed and torque control of DC motors with application to small snake robots”, IEEE/APS Intl. Conf. on Mechatronics and Robotics, 2004.

## Slide 6: Original dVRK at JHU (2004)
Low Power Motor Controller (LoPoMoCo), V2
da Vinci MTMs and PSMs

## Slide 7: Limitations of LoPoMoCo Architecture
Centralized processing and I/O
Cabling nightmare!
Required Industrial PCs with ISA bus

## Slide 8: Centralized Processing and Distributed I/O
Possible with high-performance networks/computers
  All the benefits of distributed I/O (reduced cabling)
  Computation on familiar development platform (flexibility)
Computer
(multicore)
IO
Amp
Robot
IO
Amp
IO
Amp
Power and high-speed serial network (e.g., Firewire)
Servo
Traj
App

## Slide 9: Fieldbus Requirements
Speed of at least 100 Mbits/sec
Low latency (tens of µsec)
Ability to daisy-chain
Readily available
Simple FPGA implementation
Option for high-flex cabling
IEEE-1394a (FireWire)
?
EtherCAT
Since then, other good options, such as EtherCAT
In 2006, FireWire appeared to be best choice

## Slide 10: Next Generation: Distributed I/O
IEEE1394 Snake Controller, 2008
IEEE1394 general-purpose controller, 2010
FPGA/QLA (V1)
P. Thienphrapa, P. Kazanzides, “A Scalable System for Real-Time Control of Dexterous Surgical Robots”, TePRA 2009
NSF MRI 0722943 (2007)
PI: Allison Okamura
Initial dVRK firmware comes from here

## Slide 11: System Architecture
Hardware/Firmware
Fieldbus
Real-time Control
Application
Key Concerns
Interoperability (ROS)
Performance, ease of programming
Layer
Scalability, performance
Low latency
Z. Chen, A. Deguet, R Taylor, P. Kazanzides, “Software architecture of the da Vinci Research Kit," IEEE Robotic Computing, 2017

## Slide 12: Hardware Block Diagram
Motor
Amplifier
ADC
DAC
Filter
Diff. Amplifier
Differential Receiver
Pot
Enc
Sense Resistor
Filter
+
Pot
Meas current
IEEE 1394
PHY
SPI
SPI
buffers
quad.
FPGA
read
write
Power Op Amp
-
Power Op Amp
-
Cmd current

## Slide 13: da Vinci Research Kit

## Slide 14: Ethernet Interface (V2)
Ethernet is supported everywhere, including RTOS, Simulink Real-Time (Matlab xPC)
Real-time drivers for Ethernet readily available
Linux
+ libraw1394
Xenomai
+ Rtnet
L. Qian, Z. Chen, P. Kazanzides, “An Ethernet to FireWire bridge for real-time control of the da Vinci Research Kit (dVRK)”, IEEE Conf. on Emerging Technologies and Factory Automation (ETFA), 2015.
FPGA V2.1

## Slide 15: Outline
da Vinci Research Kit (dVRK)
Next generation dVRK-Si and controller

## Slide 16: da Vinci Systems and dVRK Controllers
dVRK
dVRK-Si
da Vinci S
da Vinci “Classic”
da Vinci Si
(some)
(V1, V2, V3)
(V3)

## Slide 17: Current dVRK (V3)
Upgrade from Xilinx Spartan 6 FPGA to Xilinx Zynq 7000 SoC (FPGA + ARM processor)
  One FPGA can drive a full robot arm (up to 8 axes)
  Higher bandwidth access to low-level signals
  Could improve force estimation (and other) research
https://github.com/jhu-cisst/mechatronics-firmware
https://github.com/jhu-cisst/mechatronics-embedded

## Slide 18: dVRK Controllers
V1, V2
V3
2 FPGA/QLA board sets
(could use FPGA V3, but a waste of resources)
1 FPGA, 2 QLAs (DQLA)

## Slide 19: dVRK-Si Controller

## Slide 20: Revisiting the Controller Architecture
Current dVRK
Future dVRK

## Slide 21
Motor
ADC
DAC
Diff. Amplifier
Differential Receiver
Enc
Sense Resistor
+
measured current
position
FPGA
Power Op Amp
Power Op Amp
-
commanded voltage
quadrature
velocity
meas. torque
One channel of Quad Linear Amplifier (QLA), V1.5+
control
cmd torque
ARM
Low-Level
Control
Zynq SoC (FPGA V3+)
High-Level control
Firewire or Ethernet
Control PC
Low-Level control
dVRK Controller Electronics (dVRK-Si uses H bridge PWM)

## Slide 22: Potential Uses for Embedded Processor
Low-level control (instead of PC)
High-bandwidth data collection (~30 kHz)
“Small” neural networks (e.g., for force estimation)
Currently runs Linux; should be able to install ROS

## Slide 23: Anatomy of da Vinci S/Si
ESSJ
RAC
ESPM
ESII
Problem: Proprietary embedded devices everywhere!
Solution: create alternative firmware with open interface
(credit: Jie Ying Wu)
Solution: replace with dVRK-Si controller
(credit: Keshuai Xu)
Sensor feedback via LVDS

## Slide 24: dVRK-Si Layout
Alternative Firmware
(open protocol via LVDS)
Credit: Jie Ying Wu, Keshuai Xu

## Slide 25: Updated dVRK Setup
FPGA
QLA
QLA
dMIB
DQLA
dVRK (V3)
FPGA
FPGA
QLA
QLA
dMIB
dVRK (V1 or V2)
FPGA
DRAC
dVRK-Si
OR
PC

## Slide 26: Network Connections
Firewire and Ethernet
  Either can be used for real-time control (on FPGA)
  Ethernet also connected to embedded ARM processor
Switch
Eth1
Eth2
PS (Linux)
RT I/O
FPGA V3
PL (FPGA)

## Slide 27: System Architecture
Hardware/Firmware
Fieldbus
Real-time Control
Application
Key Concerns
Interoperability (ROS)
Performance, ease of programming
Layer
Scalability, performance
Low latency
Z. Chen, A. Deguet, R Taylor, P. Kazanzides, “Software architecture of the da Vinci Research Kit," IEEE Robotic Computing, 2017

## Slide 28: Hardware Interface (mechatronics-software)
https://github.com/jhu-cisst/mechatronics-software
Z. Chen, A. Deguet, R Taylor, P. Kazanzides, “Software architecture of the da Vinci Research Kit," IEEE Robotic Computing, 2017
Class Hierarchy for Ports and Boards
Port manages the I/O over the bus
  ReadAllBoards, WriteAllBoards can take advantage of broadcast capabilities
Board manages functionality (representation of data in buffers)
  AmpIO designed for FPGA/QLA
https://github.com/jhu-cisst/mechatronics-software/wiki/Interface-Specification

## Slide 29: Current Hardware Interface
BasePort
BoardIO
FpgaIO
AmpIO
FirewirePort
EthBasePort
EthUdpPort
EthRawPort
ZynqEmioPort
BoardIO *
Use PortFactory to construct port
Parameterized by NumMotors, NumEncoders (instead of NumAxes)
https://github.com/jhu-cisst/mechatronics-software
QLA, DQLA and DRAC
FPGA (Firewire, Ethernet, PROM)