## Slide 1: dVRK Software Overview
Anton Deguet
July 15, 2024

## Slide 2: Content
Introduction
Core components
APIs
User applications
Tools

## Slide 3: dVRKs are all different
The dVRK is a Kit.
Hardware from Intuitive Surgical, eBay or other sources:
  PSM: Patient Side Manipulator, Standard or Si
  ECM: Endoscopic Camera Manipulator, Standard or Si
  MTM: Master Tele Manipulator
  SUJ: Set Up Joints, Standard or Si
  Full surgeon console or just stereo display
  Endoscope, SD, HD or Si
dVRK controllers:
  Designed at JHU, shipped from WPI, multiple generations
  Or custom-built using PCB designs on GitHub (much harder path)
BYOPC: Bring Your Own Personal Computer
Software:
  Mostly from JHU
  Supports all dVRK configurations

## Slide 4: Technical skills required
Depending on setup:
Build 80/20 frame for the surgeon or patient side
Short pins on sterile adapters (Standard)
Build custom cables for the head sensor or camera focus controller
Build motor drive for console lift (Standard)
Get a PC with a FireWire adapter
Install Linux Ubuntu (20.04, 22.04) with ROS (1, 2)
Connect everything
Compile some code, create some configuration files
Some calibration required!
Documentation: https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki

## Slide 5: Software distribution
Source based
All repositories can be retrieved using vcs on Linux
Easy to build using catkin (ROS1) or colcon (ROS2)
Instructions:
  ROS1: https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/CatkinBuild
  ROS2: https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/BuildROS2
Can be built using CMake directly (e.g. Windows, MacOS)

## Slide 6: Software features
Written in C++, component based and multithreaded (cisst libraries)
IO, powering, safety checks, homing, position and effort control, trajectory generation using Reflexxes, actuator vs joint vs cartesian conversions, tele-operation, head sensors, focus controller…
  Configuration files for calibration and user settings
  Qt Graphical Interface (mostly visualization and debug in “direct mode”)
ROS interfaces (1 and 2), OpenIGTLink, JSON over UDP
Python (and Matlab) clients over ROS
Calibration tools
All available on GitHub
NOT FDA APPROVED, NOT FOR ACTUAL SURGERIES!

## Slide 7: Content
Introduction
Core components
APIs
User applications
Tools

## Slide 8: Software architecture
Subscribers
Publishers
MTM
PSM
MTM
PSM
mtsTeleoperation
mtsRobotIO1394
sawROS console
sawROS teleoperation
sawROS psm
sawROS mtm
sawROS io
QtConsole
sawQtTeleop
QtPSM
QtMTM
sawQtPID
sawQtIO
Single thread
SAW component
QtWidget component (optional)
ROS component (optional)
mtsPID
mtsPID
mtsPID
mtsPID
Console
mtsTeleoperation
PSM1
MTMR
PSM2
MTML
provided
required
For components, see https://github.com/jhu-cisst/cisst/wiki/cisstMultiTask-concepts

## Slide 9: Software: Console
Features
  Create components based on console configuration file (IO, PID, Arm, GUI, ROS)
  Manages state of arms and teleoperation components
Configuration files
  JSON
State
Component’s widgets
Messages

## Slide 10: Software: Console

## Slide 11: Software: IO
Features
  Convert to/from SI units
  Safety checks
Configuration files
  XML
  config-generator.py provides a template
  Stores results of calibration per arm

## Slide 12: Software: PID
Features
  PID
  Disturbance observer
  Safety checks
  Position/Effort per actuator
Configuration files
  JSON
  Default files provided

## Slide 13: Software: Arm
Features
  Homing
  Actuator to/from joints
  Joints to/from cartesian
  Provides position, velocity and effort (joint and cartesian)
  Position and effort controller (joint and cartesian)
  Instrument detection
Configuration files
  JSON
  Default files generated

## Slide 14: Software: Teleoperation
Features
  Emulate da Vinci behavior
  Nowhere as smooth but usable
Configuration files
  JSON

## Slide 15: Content
Introduction
Core components
APIs
User applications
Tools

## Slide 16: API?
dVRK API grew “organically” since 2012…
API not easy to understand for new users, hard to write your own application
Inconsistent API across devices, hard to integrate/swap devices and develop shared tools
Inconsistent API within the dVRK code base, hard to maintain for us
C++ | ROS topic | Python Client | Matlab Client
GetPositionCartesian | position_cartesian_current | get_current_position | position_current
GetPositionCartesianDesired | position_cartesian_desired | get_desired_position | position_desired
SetPositionCartesian | set_position_cartesian | move (interpolate = False) | move (interpolate = False)
SetPositionGoalCartesian | set_position_goal_cartesian | move | move

## Slide 17: API: CRTK (JHU, WPI, UW)
Standardized and documented API for robot state, move commands and operating state: https://crtk-robotics.readthedocs.io
More options to swap arms (PSM vs. JHU Eye Robot, MTM vs Omni or ForceDimension)
General purpose clients (not dVRK specific):
  ROS Python: https://github.com/collaborative-robotics/crtk-python-client
  ROS Matlab: https://github.com/collaborative-robotics/crtk-matlab-client
  For cisst/SAW “devices” (dVRK, Omni, Falcon, NDi, Atracsys…): ROS bridge, OpenIGTLink bridge, Qt Widgets..

## Slide 18: API: Operating State

## Slide 19: API: Robot Commands

## Slide 20: API: Robot Commands

## Slide 21: Content
Introduction
Core components
APIs
User applications
Tools

## Slide 22: User applications: ROS
See https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/Application-Development
Easiest approach
Choose your language with ROS bindings on the client side (C++, Python, Matlab)
Some latency but can still close the loop at high rate (~1KHz)
Subscribers
Publishers
MTM
PSM
mtsRobotIO1394
ROS console
ROS psm
ROS mtm
cisst ROS bridge (optional)
mtsPID
mtsPID
Console
MTM
PSM
User Application
(teleoperation)
dVRK Process
ROS

## Slide 23: User applications: ROS + CRTK Python Client
Subscribers
Publishers
MTM
PSM
mtsRobotIO1394
ROS console
ROS psm
ROS mtm
cisst ROS bridge (optional)
mtsPID
mtsPID
Console
MTM
PSM
User Application
(teleoperation)
dVRK Process
ROS

## Slide 24: User applications: C++
Subscribers
Publishers
sawForce
DimensionSDK
PSM
mtsTeleOperationPSM
mtsRobot
IO1394
ROS console
ROS teleoperation
ROS psm
ROS mtm
cisst ROS bridge (optional)
mtsPID
Console
MTM
PSM
See https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/Application-Development
Requires some knowledge of C++ as well as cisst libraries
Can replace or add components, either new or derived from existing ones
Payoff is very low latency, single executable
For example, replacing MTM with ForceDimension:
Subscribers
Publishers
MTM
PSM
mtsTeleOperationPSM
mtsRobotIO1394
ROS console
ROS teleoperation
ROS psm
ROS mtm
cisst ROS bridge (optional)
mtsPID
mtsPID
Console
MTM
PSM

## Slide 25: User applications: managing CPU and IO loads
Soft vs hard real-time
  dVRK software currently uses soft real-time (FireWire driver is not real-time compatible)
  With UDP, we could migrate to hard real-time. With PID on Zynq, we could also stick to soft real-time on the PC side
In practice
  If the PC is overloaded, either CPU or IOs, the dVRK software will raise errors. Unfortunately, video acquisition, disk writes are IO intensive
  Split the load on 2 PCs, use ROS between processes. One PC for ROS core, video and data collection, one PC just for the dVRK

## Slide 26: Content
Introduction
Core components
APIs
User applications
Tools

## Slide 27: Tools: Python scripts
Most tests and calibrations scripts are written using CRTK Python: https://github.com/jhu-dvrk/dvrk-ros/tree/main/dvrk_python/scripts
Examples:
  servo and move commands in dvrk_arm_test.py
  Record and replay a trajectory using ROS bag in dvrk_bag_replay.py
  Collect data over the joint space in dvrk_ecm_psm_gc_collect.py
Hand-eye calibration: https://github.com/jhu-dvrk/dvrk_camera_registration

## Slide 28: Tools: simulation (kinematic only)
Run and visualize the dVRK in Rviz
  Single arm
  Both MTMs (surgeon’s console)
  Patient side with SUJ, ECM and PSMs for Standard or Si
See https://github.com/jhu-dvrk/dvrk_model