## Slide 1: dVRK Hamlyn 2016 User meetup
Anton Deguet, Peter Kazanzides
Johns Hopkins University
June 25, 2016

## Slide 2: Outline
Group introduction
Brief history
Updates
  Hardware
    Ethernet
    SUJs
  Software
    Main features in upcoming 1.4
    Python and Matlab ROS wrappers
Future developments

## Slide 3: dVRK Sites
Hong Kong
Milan
26 groups

## Slide 4: Group introduction
Who you are
Which system are you using:
  Research Kit: 2 MTMs, 2 PSMs
  daVinci: whole system with ECM and SUJs
Research interests
  New tools
  Vision, tool tracking, imaging, US, …
  Force feedback, user UI, augmented reality, …
  Automated motion, virtual fixtures, …
What have you done so far:
  Waiting for controller or it boots!
  We just run the provided applications
  We hacked the C++ code
  It’s just another ROS node

## Slide 5: Overall goals
Stability
  Algorithms (PID, kinematics, filters)
  Efficient (memory and CPU usage)
  Safe (error checking, redundancy)
  Bug free?
Sustainability
  Leverage on existing components (ROS, RViz, Reflexxes, JsonCpp, Qt, …)
  Code re-factorization (base classes)
  Stable and consistent APIs (naming, data types)
Usability
  Interfaces (GUI, ROS, OpenIGTLink)
  Flexibility (configuration files vs compiled code)
  Extensibility (derived classes)

## Slide 6: History, 01/15 rev 1.0
Rough draft, alpha, it moves!
Somewhat stable, sustainable and usable…

## Slide 7: History, 04/15 rev 1.1
Initial feedback
  Each system is different, need more flexible parameterization
  Each user does something different, testing cases we didn’t
Urgent fixes
  Added safety checks
    Using potentiometers for safety checks
    Preload encoders, check encoder overflow
    Error propagation across components
  More and better messages to GUI and logs
Improvements
  Refactoring code (arm base class)
  Ongoing API cleanup
  LSPB trajectory generation
  FireWire broadcast
  More ROS topics (for data collection), catkin build
  Bug fixes

## Slide 8: History, 10/15 rev 1.2
Console configuration file
  Avoids many recompilations
  Simple JSON syntax https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/FileFormats
  Populates components based on configuration
    Core: IO, PID, Arm, ..
    Qt Widgets
    ROS bridges
Improved velocity estimation, better PID gains
Support for upcoming SUJ controller

## Slide 9: History, rev 1.2
More on velocity estimation
Users reported unstable control, jumps in requested current
  Initially thought that unstable IO/PID periodicity was the problem
  Velocity estimate was bad because of low encoder resolution. Usual fixes are:
    Increase refresh rate, in dx/dt this leads to higher peaks in velocities
    Increase damping in PID, also increases peaks in commanded torques
Now uses mix of:
  dx/dt where dx is position change since last read if dx > 1 and dt is time since last read (fast motion)
  1/dt where dt is time since last position change (slow motion)

## Slide 10: History, 01/16 rev 1.3
Tool configuration file
  DH, coupling, joint limits in a single file
  Coupling can be changed dynamically so trajectories can be used during homing/engage procedure, side effect is better PSM PIDs
Better homing
  Potentiometer calibration
  PSM doesn’t move if tool is present
  MTM roll limit search performed only once
Improved some safety checks to avoid false alarms
Added kinematic simulation (live demo?)
Added SetWrench methods with ROS topics

## Slide 11: History, rev 1.3
More on potentiometers
Readings are noisy and delayed
  Filtering (avg) when a precise value is needed, e.g. homing
  Redundancy check now takes time into account (fails if multiple consecutive values are off)
Calibration was off
  Calibrate scales using encoders (~2%) Important for large motions 
  Calibrate offsets using physical features
    Easy on PSM joints 4-7 (<2 degrees) Not large effect on accuracy 
    No solution yet for all others joints

## Slide 12: Hardware update: Ethernet

## Slide 13: Hardware update: SUJ
New dSIB (daVinci Setup Interface Board)
Single FPGA/QLA board for all 4 SUJs
Motor power used to release breaks
Analog inputs used to read potentiometers
Digital outputs used to:
  Control multiplexer for potentiometers, SUJs have 6 joints x 2 redundant pots x 4 arms potentiometers, QLA have 4 analog inputs
  Control PWM drive on dSIB for PSM 3 lift
Status
  Testing dSIB rev 3.0
  Have to design enclosure, mounted on patient side cart

## Slide 14: Hardware update: SUJ
QLA
dSIB
Cart

## Slide 15: Hardware update: SUJ
Potentiometer calibration
Add labels on joints (we will provide pdf)
Move to known positions, joint by joint and enter in GUI
Code computes slopes and offsets
Copy/paste output in configuration file (JSON)

## Slide 16: Hardware update: Endoscope Focus
https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/Full-da-Vinci
Control endoscope focus using dVRK digital outputs
Custom cable (done)
Software (to do)
https://github.com/jhu-dvrk/sawIntuitiveResearchKit/wiki/Full-da-Vinci

## Slide 17: Hardware updates
Heat sink for ECM/SUJ
Head sensor?

## Slide 18: Upcoming 1.4
More logic implemented in the console component
Better management of transitions between components, e.g. teleop PSM / ECM
Less code in each teleop component
Control all components from a single point (Qt Widget, ROS topics, …)
  Home, power off arms
  Start stop teleoperations, set scale
Console Qt widget stays visible

## Slide 20: Upcoming 1.4
Teleop PSM
Less events managed by component, tool clutch and operator present are handled by the console
Use new “state machine” class for a cleaner implementation, can be easily derived
Added states and transitions:
  Is PSM ready?
  Is MTM ready?
  Is MTM aligned?
Better MTM orientation lock in clutch mode

## Slide 21: Upcoming 1.4
Teleop ECM
Similar to PSM, check state of arms
Added force feedback on MTMs
  Fixed distance between MTMs
  Equal distance to eye piece
  Viscosity
Still working on ECM motion…
  Might require a new trajectory generator
  Last feature required before release

## Slide 22: Upcoming 1.4
Better ROS interfaces
Use messages with header when possible
  For example, PoseStamped instead of Pose
  Timestamps using initial cisst/SAW value
  Name in message
  Sequence number (e.g. event counting)
Added compatibility mode in dVRK ROS applications
  dvrk_console_json –c v1_3_0
  dvrk_console_json
Fix for new catkin build tool (v0.4+, also Ubuntu 16.04 with ROS Kinetic)
More topics for arms (wrench, twist), console (home, start/stop teleop, scale), teleop components…

## Slide 23: Upcoming 1.4
Better ROS wrappers
Python
  Fixed import command, uses standard ROS paths
  arm, psm, mtm, ecm, suj and console classes
  Cleanup interface
    Shorter names (move, dmove)
    Use better types (PyKDL and Numpy arrays)
  Should be stable from now on
Matlab
  Require Matlab robotic system toolbox (> 2015a, not free)
  Runs everywhere (Linux, Windows, MacOS)
  API consistent with Python API, except types are all arrays

## Slide 24: Upcoming 1.4
r = arm('PSM1);
r.position_desired % [4x4 double]
r.position_joint_desired % [7x1 double]
r.effort_joint_desired % [7x1 double
r.position_current % [4x4 double]
r.position_joint_current % [7x1 double]
r.velocity_joint_current % [7x1 double]
r.effort_joint_current % [7x1 double
r.home(); % home this arm
% move joint 1 only, index start at 1, radians
r.dmove_joint_one(-0.01, int8(3));
% move all joints, radians and meters
r.dmove_joint([-0.01, -0.01, 0.0, 0.0, 0.0, 0.0, 0.0]);
% move in cartesian space, translation only.
v = [0.0, 0.0, 0.01];
r.dmove_translation(v)
Similar commands without the [d]move prefix exist (start with move) and allow you to use absolute positions

## Slide 25: Upcoming 1.4
import dvrk
# Create a Python proxy for PSM1, name must match ros namespace
p = dvrk.psm('PSM1')
# You can home from Python
p.home()
# retrieve current info (numpy.array)
p.get_current_joint_position()
p.get_current_joint_velocity()
p.get_current_joint_effort()
# retrieve PID desired position and effort computed
p.get_desired_joint_position()
p.get_desired_joint_effort()

## Slide 26: Upcoming 1.4
# retrieve cartesian current and desired positions
# PyKDL.Frame
p.get_desired_position()
p.get_current_position()
# move in joint space
# move is absolute (SI units)
# dmove is relative
# move a single joint, index starts at 0
p.dmove_joint_one(-0.05, 2) # move 3rd joint
p.move_joint_one(0.2, 0) # first joint
# move all joints
p.dmove_joint(numpy.array([0.0, 0.0, -0.05, 0.0, 0.0, 0.0, 0.0]))
p.move_joint(numpy.array([0.0, 0.0, 0.10, 0.0, 0.0, 0.0, 0.0]))

## Slide 27: Upcoming 1.4+
These might make it to 1.4
Ethernet support
Use Reflexes/RML for trajectory generation
  Might be required for teleop ECM
  Would be nice for all commands
  Could add cartesian trajectories as well
Add ROS TF support, specially for SUJ
Better handling of redundant joints in MTMs
  We have some preliminary work with joint motion minimization and joint limits
  Issue when in gravity mode
Use new state machine in arm classes
  Current implementation is hard to maintain
  Challenging to derive from MTM, PSM, …