## Slide 1: dVRK PI / User Group Meeting
March 20, 2024
(online)

## Slide 2: Agenda
Introduction
Announcements / Events
dVRK Consortium and Community
dVRK/dVRK-Si Hardware/Software Updates
  Controllers, firmware / embedded, software
  Models and simulation
Community Presentations:
  Ken Goldberg (UC Berkeley)
  Dominic Jones (Univ. of Leeds)

## Slide 3: Announcements / Events
ISMR Workshop: “Machine Learning with the da Vinci Research Kit”, June 3, 2024 (half day)
  https://surgical-robotics-ai.github.io/ismr-2024-workshop.html
dVRK Summer School (Verona), July 2024
2023-2024 AccelNet Surgical Robotics Challenge

## Slide 4: AccelNet Surgical Robotics Challenge
Relaunch of 2021-2022 challenge
  Autonomous suturing
  Sim-to-real
Online phase
  AMBF Simulator
  Azure server
In-person phase (JHU)
  TBD
This video created via teleoperation
Challenge: Can you do it autonomously?
OISE-1927275 (WPI)
OISE-1927354 (JHU)
https://surgical-robotics-ai.github.io/surgical-robotics-challenge-2023/challenge-2023.html

## Slide 5: dVRK Consortium
Formed as a result of dVRK PI Meeting discussion
Institution and JHU sign a Consortium Agreement
Voluntary membership, with $5,000 initiation fee
  Consortium has option to decide on any future fees
Benefits of membership:
  Free replacement boards (e.g., FPGA, QLA)
  Free accessories (e.g., Dallas chip interface dongle)
  Free technical support (with a smile)
  Good karma

## Slide 6: dVRK Consortium
Finally, a (placeholder) website: https://dvrk.lcsr.jhu.edu/dvrk-consortium/
Any concerns about listing member institutions?

## Slide 7: dVRK Community
Upgrades to dVRK-Si may free up dVRK systems/controllers
  dVRK systems could be “traded in” and provided to other sites
  dVRK controllers could be repurposed for MTMs (still needed)
    PSM / ECM controllers would need a power supply change
SUJ Controllers (for dVRK)
  There is interest from at least one site. Any others?

## Slide 8: dVRK and dVRK-Si Controllers
dVRK
(V1-V3)
dVRK-Si
da Vinci S
da Vinci “Classic”
da Vinci Si
(some)

## Slide 9: Controller Build Status
Some dVRK controllers still available
  Primarily required for MTM
Second build of dVRK-Si controllers in process
  Components procured
  Ready to start final assembly

## Slide 10: Embedded Software / Firmware
FPGA V3 has Xilinx Zynq System on Chip (SoC), which has FPGA (PL) and dual-core ARM processor (PS)
PS
PL
Zynq
2 x eth
2 x fw
Companion Board
(QLA, DQLA, dRAC)
Embedded software
(Linux)
Firmware

## Slide 11: FPGA V3
FPGA
Key features:
Backward compatible with prior FPGA versions
Additional Ethernet port (2 total, 1GB each)
Linux on ARM processor (1 GB DDR3 RAM)
Micro-SD for firmware upgrades
4 additional I/O (V3.1)
DRAM
Ethernet x 2
Micro-SD
Firewire x 2
FPGA
Used for all dVRK-Si controllers and for recent dVRK controllers (since 2023)

## Slide 12: Network Connections
FPGA
FPGA
FPGA
FPGA
PC
Firewire
Ethernet
Note: Ethernet daisy-chain not yet supported by firmware
Firmware Rev 9

## Slide 13: Network Connections

## Slide 14: 1) Firewire only
FPGA
FPGA
FPGA
FPGA
PC
Firewire
Original configuration: supported by all FPGA version (V1, V2, V3)

## Slide 15: 2) Ethernet/Firewire bridge
FPGA
FPGA
FPGA
FPGA
PC
Firewire
Ethernet
First FPGA board in chain must be V2 or V3 (Firmware Rev 7+)

## Slide 16: 3) Ethernet only
FPGA
FPGA
FPGA
FPGA
PC
Firewire
Ethernet
All FPGA boards must be V3 (Firmware Rev 9+)

## Slide 17: Firmware Rev 9 Goals (in Sept 2023)
Fix Ethernet support for FPGA V3
Migrate from Xilinx ISE to Vivado for FPGA V3
  FPGA V1 and V2 only supported by ISE
Support digital current control for QLA V1.5+
Add digital (FIR) filters on analog feedback

## Slide 18: Firmware Rev 9 (expected April 2024)
FPGA V3 Ethernet support:
  4-port switch
  Implementation of “broadcast” protocols initially developed for Firewire
Minor updates:
  Fixed ECM-Si encoder preload
  Improved internal interface (EMIO bus) to PS (processor)
Internal:
  Significant refactoring of internal busses (all FPGA versions)
  Cleaned up unused files (only support CMake build)

## Slide 19: Ethernet Design
eth
PC
Different MAC addresses for FPGA and PS
Switch
Eth1
Eth2
PS (Linux)
RT I/O
FPGA V3 (ID 0)
PL (FPGA)
Switch
Eth1
Eth2
PS (Linux)
RT I/O
FPGA V3 (ID 1)
PL (FPGA)
Switch
Eth1
Eth2
PS (Linux)
RT I/O
FPGA V3 (ID 2)
PL (FPGA)

## Slide 20: Broadcast Write
DATA
HDR
DATA
HDR
DATA
HDR
PC combines data for all boards into a single packet, which is sent by Firewire broadcast or Ethernet multicast (UDP)
Each 32-bit header specifies board number and block size
Board 0
Board 1
Board 2
Firewire broadcast
or
Ethernet multicast

## Slide 21: Broadcast Read
PC sends “query” command (incl. sequence number) via Firewire broadcast or Ethernet multicast
Each board sends its data to all other boards (Firewire broadcast or raw Ethernet multicast)
PC can read all data from any one board (for Ethernet, reads from closest board)
  Header (HDR) includes block size and sequence number
DATA
HDR
DATA
HDR
DATA
HDR
Board 0
Board 1
Board 2
Firewire or
Ethernet read

## Slide 22: Embedded Software
GitHub: https://github.com/jhu-cisst/mechatronics-embedded
Released as ZIP file: fpgav3-micro-sd.zip
  Contains Linux image and all FPGA V3 firmware
  Linux app (fpgav3init) detects board type and loads correct firmware
Power Up
Load
BCFG firmware
Determine board type
Boot Linux
Load
board firmware

## Slide 23: Embedded Software Releases
1.0.0 (Aug 2023) – Initial release
1.0.1 (Nov 2023) – Minor updates
1.1.0 (April 2024)
  Firmware Rev 9
  Functional Ethernet interface on Linux
  Faster interface to FPGA registers
  Added fpgav3block / fpgav3quad utilities
  Support for cross-compiling with gcc or clang
    Can copy files to MicroSD or send via Ethernet (e.g., scp)
  Automount MicroSD to /media

## Slide 24: dVRK Software Updates
Release(s)
ROS1 and ROS2 support
Upcoming features

## Slide 25: Software: releases
2.2.0, November 2023
  OS: dropping support for Ubuntu 16.04, added 22.04
  ROS: better ROS2 support
  Hardware: DQLA and Si support
  Features:
    Better control (updated PID and teleoperation)
    More ROS topics to access internal information
    New configuration generator, generates IO, arm and console files
    Some bug fixes and some new bugs…
2.2.1, December 2023
  Bug fixes
  Minor updates

## Slide 26: Software: ROS1/2
In 2.2.x
Client side
  Added python crtk.ral to hide rospy (ROS1) and rclpy (ROS2)
  Leads to portable Python scripts to ease migration for users
  But separate repositories because catkin (ROS1) and colcon (ROS2) require different files for the build
Server side
  cisst_ros_bridge and cisst_ros2_bridge are similar but there are some differences so they are synchronized by hand
  Same applies to cisst_msgs, crtk_msgs…
  Also separate repositories for build files
Need shared build description and shared code…

## Slide 27: Software: ROS1/2 – shared build
Build process compatible with catkin and colcon
  Files used: CMakeLists.txt, package.xml, colcon.pkg (ROS2 only)
  File organization: ROS2 will find top CMakeLists.txt and assumes it’s a package. ROS1 relies on package.xml.
Solution
  File re-organization to isolate code without ROS dependencies (CMakeLists.txt only for ROS2)
  Use conditions in package.xml and CMakeLists.txt

## Slide 28: Software: ROS1/ROS2 – shared build
package.xml CMakeLists.txt

## Slide 29: Software: ROS1/2 – shared code
Introduced C++ RAL, similar to Python RAL (ROS Abstraction Layer)
Implemented in cisst_ros_bridge
#if ... #else
Macros for messages and services types
Macros over ROS log macros
Methods and classes to abstract:
  Node creation, argc/argv parsing, shutdown
  Publisher and subscriber creation
  Time computations
  …

## Slide 30: Software: ROS1/2 – last issues
ROS repositories also contain:
Models, mostly URDF and CAD files
  These seem to be shared between ROS1 and ROS2 so we should be able to merge repositories using CMakeLists.txt and package.xml with conditions
Launch files
  ROS2 introduced Python and YAML based launch files, not supported in ROS1
  ROS2 XML launch files use different tags from ROS1 launch files
  No easy solution

## Slide 31: Software: ROS1/2
End result:
For us
  Major merge, files and repositories re-organization
  Fixed some discrepancies between ROS1 and ROS2 dVRK features
  Less code and documentation to maintain, repositories to tag, etc.
For you
  Nothing different , except some files have moved
  … but ROS1 and ROS2 features available until ROS1 disappears

## Slide 32: Software: next release
Aiming for June/July, 2.3.0 with:
New firmware support
New repositories (following ROS1/2 merge)
New features:
  Hand-eye calibration
    Stereo camera calibration
    Code for hand-eye calibration
    Fixed SUJ class
  Si SUJ calibration
  Simple gravity compensation for ECM on Si
  More ROS topics

## Slide 33: Models and Simulation

## Slide 34: Instrument Models
https://github.com/jhu-dvrk/instrument-cad
Created from ISI CAD files by removing internal details
Currently, just large needle driver (420006)
Credit: Irene Kim, Haoying (Jack) Zhou, Juan Barragan, Adnan Munawar

## Slide 35: Other Models
Surgical Robotics Challenge Assets
  Suture needle
  3D-Med phantoms
Coming soon…

## Slide 36: Data Generation Pipeline
Processing and generation step
Recording step
Scene 1
Scene 2
Replay trajectories
Annotated dataset
Instrument pose
Camera parameters
Depth map
Segmented image
Instrument model
AMBF
Simulator
Teleoperation device
Recorded trajectories
rosbag

## Slide 37: Rationale for Trajectory Replay
Collect human demonstration with lower fidelity visualization
Generate higher quality (photorealistic) images for training
AMBF Visualization
(data collection)
Blender Visualization (eevee rendering)
(replay)
Blender Visualization (cycles rendering)
(replay)

## Slide 38: Community Presentations
Ken Goldberg, UC Berkeley
Dominic Jones, Univ. of Leeds